## Slide 1: Protocol: Cooling Basics, Clinical Considerations, and Phases of Care Dr. Frank Moler

## Slide 2: Overview
This talk reviews basic temperature (temp) related information needed for P-ICECAP.
There is much information to know. Key content is repeated. (Sorry, no “Greatest Movies of All Time” trivia breaks as in THAPCA). Periodic review will be required during the trial.
The information presented will assist the research team in safe monitoring and application of cooling in our study subjects.
‘Just in time’ reviews with the clinical teams will be optimal, especially for the Induction of cooling and the Rewarming phases of P-ICECAP.

## Slide 3: Outline
Definitions
Thermoregulation - basics
Physiologic and other clinical effects of hypothermia/cooling
Central temperature measurement
Factors impacting target temperature
Cooling protocol through 120 hours
Review/Checklist (extra)
Cases (extra)

## Slide 4: Definitions

## Slide 5
Polderman
CCM 2009

## Slide 6
Irwin and Rippe. Intensive Care Medicine, 4th ed, 1999
*Concern for arrhythmias at temp < 30°C. Rewarm STAT to goal
**Greatly increased risk of VF and other arrhythmias < 28°C. STAT rewarming required.
Therapeutic Normothermia
= Normothermia
TTM 36.0-37.5°C (36.8)
Therapeutic Hypothermia
= Cooling
TTM 32.0-34.0°C (33.0)

## Slide 7: Thermoregulation Basics 101

## Slide 8: Normal Thermoregulation
Heat production
  Normal heat production from metabolic processes in liver, viscera, and muscle
  During exercise or shivering, muscle primary source of heat generation, may be very large
Heat elimination
  Radiation = heat from skin to object without contact (NA)
  Convection = airflow across skin (minor P-ICECAP)
  Conduction = skin to object in contact (#1 in P-ICECAP)
  Evaporation = sweating (NA in P-ICECAP)

## Slide 9: Normal Thermoregulation
Hypothalamus regulates body Tº
  Afferent inputs to hypothalamus
    Skin*, abdomen, thorax, spinal cord, brain
  Hypothalamus processes based on its setpoint
  Central temp below hypothalamic setpoint results in efferent responses
    Cutaneous vasoconstriction
      impedes heat transfer through skin
    Shivering
      generates heat (muscles)

## Slide 10
Sessler DI. NEJM 1997:336;1730-7

## Slide 11: Thermoregulation
Pediatrics
  Smaller infants / children
    Larger SA/volume compared to adults
    Reduced shivering response < 1 yr
    Easier/shorter time to induce hypothermia (cooling) and temp control in very young
Shivering decreases at approximately 33.5ºC
  P-ICECAP goal 33.0ºC in hypothermia (cooled) groups

## Slide 12: Normal thermoregulation
Normothermia Phase
  If hypothalamic set point is elevated (e.g., fever at 39ºC) relative to a goal temp 36.8ºC, one will see similar physiologic responses as Therapeutic Hypothermia (cooling) induction phase
    Vasoconstriction
    Shivering
  Common etiologies of increased set point (fever)
    Post-cardiac arrest syndrome
    Infection
Normal temp range is ~36.5-37.5ºC during a day.
  Cooling devices sensitive to approx. ± 0.2ºC from set point.
  They will attempt to warm and cool normal subjects!

## Slide 13: Physiologic and Other Effects of Cooling in P-ICECAP

## Slide 14: List of Physiologic Effects
Shivering
Hypovolemia (during cooling and rewarming)
CV including bradycardia
Potassium
Glucose
Other chemistries (Mg, PO4, etc.)
LFTs, amylase/lipase, lactate
Plts/Coags
WBC/Inflammation/Infection
Drug metabolism
Metabolic rate
Blood gases
Skin
Modified from:
- Polderman, CCM 2009
- ILCOR, Circulation, 2008

## Slide 15: 1. Shivering
Frequent, causes heat generation and rewarming
Tx (REQUIRED)
Suggested agents
  Opioids (e.g., fentanyl)
  Benzodiazepines (e.g., midazolam) and others
  NMB (e.g., vecuronium)
Shivering response decreases at ~ 33.5ºC
Shivering response less in young (< 1 yr)
Will see shivering in both hypothermia (cooled) and normothermia phases, if hypothalamic set point is greater than goal temperature
May or may not be visible

## Slide 16: 1. Shivering – drugs to inhibit
Benzodiazepines* (midazolam - example)
  Sedative
  Vasodilation (+/-)
  Antiepileptic effects
  Decrease shivering
Opiods* (fentanyl - example)
  Analgesia, sedation
  Vasodilation (+/-)
  Decrease shivering
NMB* (vecuronium, rocuronium and others). Cis-Atracurium has temperature dependent metabolism, prolonged with cooling (Hofmann Reaction). Twitch monitoring with infusions.
  Inhibits shivering, facilitates cooling and temperature control
  Masks sedation level and seizures
*ILCOR, Circulation 2008 – drug classes recommended

## Slide 17: Induction of Hypothermia without sedation
If hypothalamic set point normal at 37.0ºC
- Vasoconstriction - 36.5ºC
- Shivering - 35.5ºC
-↑HR
-↑Metabolic rate (40-100%)
-↑Stress response
Undesirable in patients with neurologic and/or post hypoxic injury
Increased risk of adverse cardiac events
Polderman
CCM 2009

## Slide 18: Induction of Hypothermia with sedation/analgesia
↓Shivering
↓HR
↓ Metabolic rate
↓ Stress response
Improved neurologic outcome compared to no sedation/analgesia.
‘Proper sedation & analgesia are important for successful use of cooling’ (Polderman 2009).
Polderman
CCM 2009

## Slide 19: 2. CV: Hypovolemia
Hypovolemia – common during the cooling Induction Phase
  often due to cold diuresis (renal);
  results in tachycardia and hypotension;
  requires tx
  Note: if patient cooled and HR not reduced, may be sign of hypovolemia
Hypovolemia – also common during Rewarming Phase
  Vasodilation; may result in tachycardia and hypotension; requires tx

## Slide 20: 3. CV effects
Cardiovascular (assuming pt deeply sedated and euvolemic)
  - ↑ BP (MAP), ↑ CVP, ↑ MV02
  - ↓ HR
  - ↓ CO (due to HR), but improved O2 supply/demand ratio
    Case series – cooling used for low cardiac output states (LCOS)
    Used for JET post op ped cardiac patients

## Slide 21: 3. CV effects
ECG changes –
  Bradycardia (🡻HR) common (🡹PR, 🡹 QRS,🡹QT intervals)
  No specific tx usually required for 🡻HR, if temp >30ºC and otherwise stable
    Atropine ineffective
    If hypothermic without 🡻HR, consider hypovolemia or inadequate sedation as cause
  Other arrhythmias uncommon if temp > 30ºC!
  Arrhythmias at temps < 30ºC
    28-30 ºC - 🡹 (AF & VF)
    < 28 ºC - 🡹🡹VF.
    STAT rewarming required if <30ºC (MANUAL Mode required for Blanketrol-III)

## Slide 22: 4. Electrolytes (Potassium = K+)
Close monitoring of K⁺ required post arrest due to AKI risk
Electrolytes q 6 hr during cooling and rewarming phases and q 12 hr during other phases
  Induction Phase - serum K⁺ decreases
    Careful replacement as needed
  Rewarming Phase - serum K⁺ increases
    Slow rewarming results in less elevation in K⁺
    If patient received insulin for hyperglycemia and extra K⁺ replacement given, this may result in greater ↑ K⁺ on rewarming – be careful
    Consider removing K⁺ from IV fluids during rewarming; supplement prn only if needed

## Slide 23: 5. Hyperglycemia (GLU)
Common post arrest due to stress response
Relative insulin resistance with cooling
Significance & optimal range for GLU unknown
Neonatal, adult and THAPCA RCTs did not use tight control
Often improves without tx in first 24 hr
Important: if insulin for hyperglycemia used during cooling, will need more K+ replacement. This may lead to HYPERkalemia and HYPOglycemia on rewarming as insulin resistance resolves.
Protocol suggests <200 mg/dl (range 80-200) acceptable
  consider reducing glucose in IV solutions, insulin only as needed for GLU > 200.
Monitor q 6-12 hr. More often if insulin used.

## Slide 24
6. Chemistries (other)
  ↓ Phosphate, Magnesium, Calcium
    Each may decrease during cooling
    Monitored at least daily
    Replace if indicated
7. LFTs, Amylase/Lipase, Lactate
  ↑ Amylase, lipase, liver enzymes
  ↑ Lactate (up to 6 mmol/L)
    Monitor at least daily
    No tx generally required
    Elevations also commonly associated with cardiac arrest

## Slide 25: 8. Hematology/Coagulation
Platelets
  Mildly reduced numbers common
  May require tx [platelet transfusion] if level too low for clinical setting (e.g., chest tube bleeding).
Mild abnormalities coagulation studies ~ 33ºC
  NOT seen when measured in lab (37ºC)
  Usually requires no tx [FFP transfusion]
Clinical trials including THAPCA-IH did not describe increased bleeding with cooling.
Monitor at least daily

## Slide 26: 9. Hematologic (Neutropenia)/Infection
↓ WBC (neutropenia) may occur
Impaired inflammatory response with cooling
Potentially higher risk of infection
Out of hospital cardiac arrests commonly associated with VAP and/or BSI in adults
THAPCA overall positive cultures 39-46% (lung, blood and urine). Drowning subgroup 43-67%
IMPORTANT:
Consider antibiotic prophylaxis in BOTH cooled & normothermia groups as fever will be masked in both.

## Slide 27: 10. Drug Metabolism
Drug clearance often dependent on enzyme reactions
Hypothermia is expected to be associated with slower drug clearance and potentially higher drug levels (opiates, benzos, NMBs, etc.).
  Follow levels if available (i.e., phenobarb)
  Titrate sedation drugs to effect
  Consider cautious use of drugs that cause bradycardia (i.e., dexmedetomidine?)

## Slide 28: 11. Metabolic Rate
Reduced with cooling (32-34ºC)
  ~8-10% per degree C
Caloric requirements decrease during cooling
  ~30-40%
Do not over feed

## Slide 29: 12. Blood Gases
PaO2 and PaCO2 solubility differs by temp
Controversial if correction should be done
P-ICECAP, like THAPCA, will not temp correct ABGs
Report at standard body temp 37.0ºC
A rough estimate of temp correction to 33ºC
~ PaCO2 = ↓2 torr/ºC = ~ 8 torr
~ PaO2 = ↓5 torr/ºC = ~20 torr

## Slide 30: 13. Skin
Closely observe skin and provide good nursing care during 120 hrs. of temperature management.
  Cooling not associated with skin break down in Neonatal cooling trials up to 72 hr. or THAPCA 48 hr.
Larger, malnourished, immobile patients may be at greater risk

## Slide 31: Central Temperature Measurement

## Slide 32: Temperature Measurement
Central temperature measurement required to estimate blood temp (Gold Standard)
Delay in a central site to reflect blood temp in real time is associated with overshoot of cooling
  - Ideal site = accurate, short time lag
Dual central temp measurements required for all patients (Primary to cooling device; Secondary to bedside monitor or cooling device).
Exception - ECMO cases – 1 central temp (or venous circuit blood) only required

## Slide 33
Esophageal (Preferred primary site – attached to the cooling devise (Arctic Sun, Blanketrol, other). Used as sole temp site in NICHD neonatal trials
  Accuracy: High level
  Time lag: Shortest = 5 min (2-10 min)
  Insertion: easy, but need to verify position
  IMPORTANT: Correct placement in lower 1/3 of esophagus is critical
    If in stomach, temp may measure low by 1-3ºC
    If tube feeds (gastric) and reflux, may make measurement inaccurate
    Vented G-tube accuracy?

## Slide 34
Rectal (secondary probe– to monitor)
  Accuracy: Moderate level
  Time lag: Moderate = 15 min (10-40 min)
  Insertion: Easy
  Dislocation: Common. Monitor for it.
Bladder (secondary probe – to monitor)
  Accuracy: Moderate level
  Time lag: Moderate = 20 min (10-60 min)
  Insertion: Easy
  Dislocation: Uncommon. Low urine output may result in less accurate measurements
  Not available for smallest infants
*If Esophageal probe is not used as primary probe, then Rectal or Bladder will need to be selected.

## Slide 35
Skin sites (skin, axillary, etc)
  Accuracy: Inaccurate – not a central temperature. Do not use.
  Time lag: Moderate = 20 min (10-60 min)
  Insertion: Easy
  Dislocation: Uncommon
Tympanic membrane (better than Skin)
  Accuracy: Moderate, may be inaccurate
  Time lag: Moderate = 10 min (10-20 min)
  Insertion: Easy; quick
  Dislocation: NA
  Other: not continuously measured

## Slide 36: Central Temp Differences
Two central temps for safety
If within ± 1ºC - acceptable
If consistently > 1ºC, escalating action required
  Notify the site PI
  Verify probe placement (esophageal, rectal)
  Verify YSI 400 compatible probes used
  Stomach feeds/GE reflux (esophageal probe)
  Low urine output (temp sensing Foley)
  Determine which probe is most accurate to be Primary connected to the cooling device.

## Slide 37: Factors influencing ability to maintain goal temperature

## Slide 38: 1. Patient factors
Patient factors impeding cooling
  Size (larger, obesity)
  Shivering (commonly subclinical)
    Sedation/analgesia/NMB (Inadequate)
    Sepsis/Infection
  Seizures
  Extremely reduced CO/poor skin perfusion

## Slide 39: 2. Skin surface area for cooling
Surface area for contact (Conduction)
  2 vs. 1 blankets (i.e., anterior/posterior vs. posterior)
  Positioning of patient (i.e., side vs. back)
  Probably less of issue with Arctic Sun pads
Extraneous materials between patient and blankets/pads (Maxi-Therm Lite or Arctic Sun pads)
  Minimize, none required, no sheets

## Slide 40: 3. Cooling Devices
Know how to use your cooling device per the manufacturer's recommendations!
Also, know important limitations of your device
Most common devices used in P-ICECAP are:
  Blanketrol-III: Gentherm (formerly CSZ) has improved educational materials and videos on website.
  https://www.gentherm.com/en/medical/hyper-hypothermia/blanketrol-3
  Arctic Sun: BD outstanding hands-on customer service
  Other (Criticool, etc.)
Unlike THAPCA, we are not instructing on the use of any device. Examples used are for discussion purposes only.

## Slide 41: 3. Cooling Equipment: Example of modes – Blanketrol-III
AUTO CONTROL Mode
  Warms or cools water to max range of 4 - 42ºC when patient’s central temp +/- 0.2ºC from Blanketrol Set Point temp.
  For large patients.
GRADIENT VARIABLE MODE (Plus SMART MODE)
  Warms or cools water to narrower range; dampens temp fluctuation compared to AUTO CONTROL Mode.
  For smaller patient sizes.
  Example (assume patient 34ºC and set point 33ºC )
    AUTO CONTROL: 4 - 42ºC For large patients
    Gradient Variable 20ºC: 14 - 42ºC
    Gradient Variable 10ºC: 24 - 42ºC. For smallest patients
Defer to manufacturer/vendor for optimal set up and use

## Slide 42: Temperature Tracings (from Primary Probe)
Not in range
AUTO Mode
NMB, Sedation
In range
GRADIENT VARIABLE Mode 10º C
NMB, sedation

## Slide 43: 3. Blanketrol and SMART MODE
GRADIENT VARIABLE with SMART MODE – Blanketrol-III
A modification to the GRADIENT VARIABLE MODE.
SMART MODE will decrease the water temperature set in GRADIENT VARIABLE MODE by 5ºC if the goal temperature is not achieved within 30 minutes.
It reverts to the GRADIENT VARIABLE MODE once the target temperature goal is achieved.
This mode is suggested to be used by the manufacturer (Gentherm).
See User Guide and Inservice videos updated since THAPCA.
https://www.gentherm.com/en/medical/hyper-hypothermia/blanketrol-3

## Slide 44: 3. Blanketrol-III
Manual Mode - Blanketrol-III
  Not normally used except for emergencies
  IMPORTANT: Key fact to know for Blanketrol! Manual mode is required if patient's (pt) tempis ever ≤30°C
    None of the other Blanketrol Modes function if patient temp is ≤30°C
    Suggest setting the Manual Mode to highest (warmest) setting (42°C) briefly until the pt temp is 33°C. Then use Auto Control of a Gradient Variable SMART Mode depending on patient size
*IMPORTANT - In the Manual Mode, the bedside nurse must continuously observe the pt’s temp. The pt is 100% dependent on careful temp titration by nurse.

## Slide 45: Protocol Overview Through 120 Hours

## Slide 46: Overview – from 37,000 feet
Example – University of Michigan PICU
PICU fellow is contacted re: an OHCA from outside ED or our UM ED.
The research team on call is immediately notified of a pending OHCA admit.
Research team discusses with clinical team the case summary, arrival time, and approach for consent
Order for nursing to get cooling equipment to bedside:
  Blanketrol-III, two Maxi-Therm Lite cooling blankets (Ped or Adult), 2 hoses, 2 temperature probes and temp sensing Foley of correct size
On pt arrival, clinical team stabilizes, places CVC, art line.
Cooling device started as soon as it is safe to do so.
Clinical team initiates their usual TTM target between 33-37ºC before consent.

## Slide 47: Overview – from 37,000 feet
Research team gets informed consent and randomizes to 1 of 3 cooling durations (24, 48 or 72 hrs) for first 150 pts (“burn-in” phase).
Subject enrollment = time randomized to a study cooling duration.
TTM 33°C will be set as the target temp no later than 15 min following randomization.
  If it was started prior to randomization, then the start time for cooling will be when a target 32-34°C range was set.
Protocol goal is to achieve a temp range of 32-34°C no later than 2 hr. after randomization.
  Sedation and NMB for induction phase results in fastest time to goal

## Slide 48: Overview – from 37,000 feet
Cooling duration is equal to the combined time of the Induction plus Maintenance phases.
After the cooling duration is completed, slow rewarming over at least 16 hrs. is done.
Then normothermia 36.8°C for rest of 120 hr.

## Slide 49: Durations of Cooling in P-ICECAP Patient Timeline 0 - 120 Hours

## Slide 50: Cooling Duration
Different than how it was defined in THAPCA.
Cooling duration - Induction Phase + Maintenance Phase combined times. Starts when cooling device is set at target of 33°C [32-34 °C]. Ends when planned rewarming starts.
Induction phase – starts when cooling device is set to the target temperature of 33°C post randomization (or 32-34°C range pre-randomization) and ends when the range of 32-34°C is achieved. Goal < 2 hrs.
Maintenance phase – the remaining time to complete the assigned cooling duration. Ends at the start of rewarming.
For the first 150 patients in P-ICECAP, the cooling durations will be 24, 48 or 72 hours only. (All patients cooled). Other cooling durations (0 to 96 hrs.) will be added in Year 3.
DCC will provide sites with the exact time to begin rewarming.

## Slide 51
Timepoints | 
a | randomization to Hypothermia (blue) or Normothermia (gray)
a - b | interval to assigned temperature goal range
a - c | duration of cooling assigned in hr
c - d | rewarming of cooled group
d - e | interval of controlled normothermia through 120 hr
e | end of study temperature control
24 Hour Cooling Duration

## Slide 52
Timepoints | 
a | randomization to Hypothermia (blue) or Normothermia (gray)
a - b | interval to assigned temperature goal range
a - c | duration of cooling assigned in hr
c - d | rewarming of cooled group
d - e | interval of controlled normothermia through 120 hr
e | end of study temperature control
48 Hour Cooling Duration

## Slide 53: 72 Hour Cooling Duration
Timepoints | 
a | randomization to Hypothermia (blue) or Normothermia (gray)
a - b | interval to assigned temperature goal range
a - c | duration of cooling assigned in hr
c - d | rewarming of cooled group
d - e | interval of controlled normothermia through 120 hr
e | end of study temperature control

## Slide 54: Review: Cooling Duration
Duration of cooling starts when the target temperature on the cooling device is set to 33°C (range 32-34°C)
Goal: start 33°C target temperature <15 minutes post randomization.
If cooling device’s set temp is between 32-34°C before randomization (because this is the site TTM practice), then the start time for duration of cooling is pre-randomization. After randomization, the target should be set at 33°C.
Duration of cooling ends at the start of planned rewarming
Equals Induction + Maintenance combined time

## Slide 55: Temperature Monitoring and Management

## Slide 59: Monitoring: TTM 33°C (32-34°C)
Two central temperature probes.
  Primary to cooling device (Blanketrol-III, Arctic Sun, other).
    *This temperature is entered into the case report form (CRF).
  Secondary to bedside monitor or device (safety).

## Slide 60: Monitoring: TTM 33°C (32-34°C)
Cooling device’s target temp is 33°C (range 32-34°C) until rewarming. Different devices have different settings/modes for small to large sized patients.
  If temp is not staying in the 32-34°C range, need to adjust cooling device per manufacture (e.g., next slide).
    Arctic Sun (excellent hands-on support)
    Blanketrol-III (good online instructions & videos)
    Both have 24/7 hotline numbers for support.
  The on-call P-ICECAP team has 24/7 hotline that is available for other study questions.
  We will collect temp information hourly after the first central temp probe is placed until end of TTM or the probe is removed. (FDA request).

## Slide 61: Temperature tracings from small child (primary probe)
Not in 32-34ºC range
AUTO Mode
NMB, Sedation
In range
GRADIENT VARIABLE Mode 10ºC
NMB, sedation

## Slide 62: Temperature Management
A major goal in P-ICECAP is to achieve the desired phase target temperatures for the 120-hour intervention while preventing shivering.
Sedation and analgesia are generally used throughout the120 hours while a patient remains intubated.
NMB use for Induction and Rewarming phases. Other times PRN.
Subclinical shivering is common. In patients with difficult to maintain temperature, consider sedation with NMB trial.

## Slide 63: Temperature Management
Sedation/analgesia and NMB for Induction Phase until a stable goal 33°C target.
  The goal clinical response is “sluggish or no response to noxious stimulus.”
    Common sedatives midazolam and dexmedetomidine.
    Common analgesics fentanyl and morphine.
    Common NMB agents vecuronium and rocuronium.
      Twitch monitoring as needed
    Infusions and intermittent dosing per site practice
After the goal temperature range is achieved and stable, may hold NMB and dose prn through the Maintenance Phase. Titrate sedation/analgesia to above goal.

## Slide 64: Temperature Management
Sedation/analgesia and NMB are also key during the Rewarming Phase. This facilitates slow controlled temp increase to the normothermia target 36.8 °C.
Increased doses of sedatives/analgesics and NMBs may be required during rewarming as drug clearance increases at higher temperatures.
See Clinical Practice Guidelines

## Slide 65: P-ICECAP Trial: Cooling, Rewarming and Normothermia Phases

## Slide 66: Cooling Groups: 24, 48, and 72 hour
Induction Phase (I)
  Time from start of TTM 33ºC (or 32-34ºC if pre randomization) until the goal range (32-34ºC) is reached.
  Use the recommended cooling modes described by manufactures for the patient’s size.
    Blanketrol III - AUTO CONTROL or GRADIENT VARIABLE SMART MODE – per manufacturer.
    Arctic Sun – per manufacturer.
  Induction will require sedation + analgesia and NMB
  Likely time of maximum BP instability following OHCA since closest to event
  Hypovolemia, Hypokalemia and Hyperglycemia may occur during this period
  Review issues with clinical team optimal

## Slide 67: Cooling Groups: 24, 48, and 72 hour
Maintenance Phase (II)
  Steady state period with target temperature 33ºC (32-34ºC) until assigned study cooling duration is completed and planned rewarming starts.
  Adjust the cooling device mode as needed per manufacturer.
  Titrate sedation/analgesia to achieve/maintain “sluggish or no response to noxious stimulus.”
  NMB prn after stable 32-34ºC temp range is achieved.
  Similar clinical issues as Induction Phase possible (Hypovolemia, Hypokalemia and Hyperglycemia).

## Slide 68: Cooling Groups: 24, 48, and 72 hour
Rewarming Phase (III)
  This is a critical time – it needs to be done slowly.
  Begins with the initiation of planned increase of device target temperature toward 36.8ºC (normothermia) goal.
  Should be done over ≥16 hrs
  For Blanketrol-III: AUTO CONTROL or GRADIENT VARIABLE SMART MODE
    Manually Increase temp set goal 0.7 ºC every 4 hrs.
      33ºC (0 hr); 33.7ºC (0-4hr); 34.4ºC (4-8hr); 35.1ºC (8-12hr); 35.8ºC (12-16hr); then 36.8ºC (16+hr)
    Goal temp of 36.8ºC (36-37.5ºC range) after 16 hrs
  For Arctic Sun – the rate of rewarming is programed to achieve the goal of 36.8ºC (from 33ºC) over 16-18 hr.

## Slide 69: Cooling Groups: 24, 48 and 72 hour
Normothermia Phase (IV)
  Goal temp is 36.8°C, range 36-37.5°C for remaining time to 120 hrs
  If clinical team determines they must check fever status, put in MONITOR ONLY Mode
  Return to the device’s appropriate cooling mode if temp > 37.5°C, but only if the patient remains intubated. Sedation/analgesia and possibly NMB may be required to prevent shivering

## Slide 70: Cooling Groups: 24, 48, and 72 hour
Normothermia Phase (IV)
  Clinical team may elect to extubate patient if clinically awake and otherwise stable
    Management of fever following extubation is limited to antipyretic agents (Tylenol). Will NOT be able to deeply sedate or use NMB to prevent shivering.
    If afebrile, could use MONITOR Only Mode
  *IMPORTANT: Do NOT extubate a patient until rewarmed! Cerebral edema, hypoglycemia, hyperkalemia, and hypotension are risks of rapid rewarming.

## Slide 71: Initial Site Enrollments
For the first 2 patients enrolled from each site, we recommend you contact the on-call 247 P-ICECAP hotline to review the Induction Phase soon after device is set to 33°C. Call again just prior to start of the Rewarming Phase.
This was done successfully in THAPCA.
Since sites are using their own cooling devices, we are relying on sites and manufacturers to have expertise for using their cooling equipment safely. Contact your vendor for an in-service if you believe it would benefit your PICU/PCCM team.
Arctic Sun may have already contacted you.
Contact Gentherm (Blanketrol) and other manufactures as needed for in-services.

## Slide 72: Questions?